Biophysics Lecture Tuesday, February 12th, 2019
Presenter: Borries Demeler
Topic:
Sedimentation Transport II
Copy of Lecture at:
https://demeler.uleth.ca/biophysics/archive/Demeler/

---
Transport Processes – Partial Specific Volume and Buoyancy

---
Transport Processes – Partial Specific Volume and Buoyancy
Whenever there is binding, the vbar will correspond to the vbar of the sedimenting particle, and must include all components bound to the molecule of interest. Likewise, the molecular weight will increase due to the binding event.
left ( 1 - %PHI %rho right )_sp `=` left ( 1 - {bar {%nu}}_prot `%rho right ) `+` %delta_det left ( 1 - {bar {%nu}}_det `%rho right ) `+` ...

---
Transport Processes – Partial Specific Volume and Buoyancy
In this nanodisk assembly, the sedimenting particle consists of a membrane protein, phospholipids, belt protein and any ions and solvent molecules attached to them.

---
Transport Processes – Partial Specific Volume and Buoyancy
Strategies for measuring MW of proteins when detergent is bound:
Change the solvent density so that the solvent density is equivalent to the detergent density. Both detergent density and solvent density need to be independently validated. If both are the same, the bound detergent will not contribute to the buoyancy of the molecule, and:
      Then the detergent will not contribute.
If the density of the detergent cannot be matched by any heavy water concentration, the same principle can be used by making multiple measurements in different concentrations of D2O or H2O18 and evaluating the buoyancy term. Plot the buoyancy term as a function of solvent density and extrapolate this function to the density of the detergent. At this point the buoyancy term only reflects the protein, and the molecular weight reflects the entire sedimenting particle.
%rho `=` 1 / {bar %nu}_det " where: " %delta_det left ( 1 - {bar {%nu}}_det `%rho right )`=` 0 " and" newline M left( 1 - %PHI %rho right )`=` M left ( 1 - {bar %nu }_prot %rho right )

---
Transport Processes – Partial Specific Volume and Buoyancy
s_{20,W} ~=~ s_{T,B} {left ( 1- bar %nu %rho right )_{20,W} ` %eta_{T,B}} over {left ( 1- bar %nu %rho right )_{T,B}` %eta_{20,W}}

---
Relationship between M, f, φ, s, and D
matrix { alignl {color red {bold f}} # {~=~} # alignl {{RT} over {N color red {bold D}}} ## {alignl color red {bold M}} # {~=~} # alignl {{color red {bold s} N color red {bold f}} over {1 - bar %nu %rho}} ## alignl {color red { bold V}} #{~=~} # {alignl { color red {bold M} bar %nu} over {~N}} ## alignl {color red { bold r_0 }} # {~=~} # alignl {left( {3 color red {bold V}} over {4 %pi} right)^{1/3} } ## alignl {color red {bold f_0}} # {~=~} # alignl { 6 %pi %eta color red {bold {r_0}}} ## alignl {color red {bold %phi}} # {~=~} # alignl { color red bold {f} over color red bold{f_0}} }
left ( {partial C} over {partial t} right ) `_r ~ = ~ { - `1} over r partial over {partial r}~ left [` s %omega^2 r^2 C~-~ D r` {{partial C} over {partial r } }` right ] `_t
Concentration Sedimentation Diffusion

---
Relationship between M, f, φ, s, and D
matrix { alignl {color red {bold f}} # {~=~} # alignl {{RT} over {N color red {bold D}}} ## {alignl color red {bold M}} # {~=~} # alignl {{color red {bold s} N color red {bold f}} over {1 - bar %nu %rho}} ## alignl {color red { bold V}} #{~=~} # {alignl { color red {bold M} bar %nu} over {~N}} ## alignl {color red { bold r_0 }} # {~=~} # alignl {left( {3 color red {bold V}} over {4 %pi} right)^{1/3} } ## alignl {color red {bold f_0}} # {~=~} # alignl { 6 %pi %eta color red {bold {r_0}}} ## alignl {color red {bold %phi}} # {~=~} # alignl { color red bold {f} over color red bold{f_0}} }
Shape
Dependence
left ( {partial C} over {partial t} right ) `_r ~ = ~ { - `1} over r partial over {partial r}~ left [` s %omega^2 r^2 C~-~ D r` {{partial C} over {partial r } }` right ] `_t
Concentration Sedimentation Diffusion

---
Relationship between M, f, φ, s, and D
matrix { alignl {color red {bold f}} # {~=~} # alignl {{RT} over {N color red {bold D}}} ## {alignl color red {bold M}} # {~=~} # alignl {{color red {bold s} N color red {bold f}} over {1 - bar %nu %rho}} ## alignl {color red { bold V}} #{~=~} # {alignl { color red {bold M} bar %nu} over {~N}} ## alignl {color red { bold r_0 }} # {~=~} # alignl {left( {3 color red {bold V}} over {4 %pi} right)^{1/3} } ## alignl {color red {bold f_0}} # {~=~} # alignl { 6 %pi %eta color red {bold {r_0}}} ## alignl {color red {bold %phi}} # {~=~} # alignl { color red bold {f} over color red bold{f_0}} }
Size
left ( {partial C} over {partial t} right ) `_r ~ = ~ { - `1} over r partial over {partial r}~ left [` s %omega^2 r^2 C~-~ D r` {{partial C} over {partial r } }` right ] `_t
Concentration Sedimentation Diffusion

---
Relationship between M, f, φ, s, and D
matrix { alignl {color red {bold f}} # {~=~} # alignl {{RT} over {N color red {bold D}}} ## {alignl color red {bold M}} # {~=~} # alignl {{color red {bold s} N color red {bold f}} over {1 - bar %nu %rho}} ## alignl {color red { bold V}} #{~=~} # {alignl { color red {bold M} bar %nu} over {~N}} ## alignl {color red { bold r_0 }} # {~=~} # alignl {left( {3 color red {bold V}} over {4 %pi} right)^{1/3} } ## alignl {color red {bold f_0}} # {~=~} # alignl { 6 %pi %eta color red {bold {r_0}}} ## alignl {color red {bold %phi}} # {~=~} # alignl { color red bold {f} over color red bold{f_0}} }
Anisotropy
left ( {partial C} over {partial t} right ) `_r ~ = ~ { - `1} over r partial over {partial r}~ left [` s %omega^2 r^2 C~-~ D r` {{partial C} over {partial r } }` right ] `_t
Concentration Sedimentation Diffusion

---
Relationship between M, f, φ, s, and D
matrix { alignl {color red {bold f}} # {~=~} # alignl {{RT} over {N color red {bold D}}} ## {alignl color red {bold M}} # {~=~} # alignl {{color red {bold s} N color red {bold f}} over {1 - bar %nu %rho}} ## alignl {color red { bold V}} #{~=~} # {alignl { color red {bold M} bar %nu} over {~N}} ## alignl {color red { bold r_0 }} # {~=~} # alignl {left( {3 color red {bold V}} over {4 %pi} right)^{1/3} } ## alignl {color red {bold f_0}} # {~=~} # alignl { 6 %pi %eta color red {bold {r_0}}} ## alignl {color red {bold %phi}} # {~=~} # alignl { color red bold {f} over color red bold{f_0}} }
  Partial specific
  volume and
  density
left ( {partial C} over {partial t} right ) `_r ~ = ~ { - `1} over r partial over {partial r}~ left [` s %omega^2 r^2 C~-~ D r` {{partial C} over {partial r } }` right ] `_t
Concentration Sedimentation Diffusion

---
Background – Analytical Ultracentrifugation
Information Available from Sedimentation Velocity Experiments:
Sedimentation coefficient
Diffusion coefficient (translational)
Molecular mass (PSV must be known)
Frictional coefficient
Frictional ratio (MW or PSV must be known)
Stokes radius
Density or partial specific volume
Partial concentration of a solute
Equilibrium constants (Kd)
Rate constants (slow reactions)

---
Background – Analytical Ultracentrifugation
What is Analytical Ultracentrifugation (AUC)?
A technique to separate macromolecules dissolved in solution in a centrifugal force field. AUC can “watch” the molecules while they are separating and identify and differentiate them by their hydrodynamic properties and partial concentration. AUC is a “First Principle” method, which does NOT require standards.
 How does AUC work?
By applying a centrifugal force, molecules are separated based on their buoyant mass and their frictional properties. The molecules are observed using different optical systems that detect different properties of the molecules, such as refractive index, UV or visible absorbance, or fluorescent light emission.
What molecules can be studied?
Virtually any molecule, colloid or particle that can be dissolved in a liquid can be measured by AUC, as long as it does not sediment by gravity alone (nucleic acids, proteins, carbohydrates, peptides, nanoparticles, synthetic polymers, small molecules, lipids, viruses). The molecule or particle can be as small as salt ion, or as large as an entire virus particle → very large size range (102 – 108 Dalton).
The ultracentrifuge can spin at 60,000 rpm, generating forces as high as 250,000 x g. Even small molecules will sediment in such a force.

---
Background – Analytical Ultracentrifugation
What can be learned from AUC?
Excellent method for characterizing any molecule or molecular interaction in the solution environment – small sample requirement, up to 14 samples can be analyzed. Analysis is based on first principles - No standards are required
Molecules can be studied in a physiological environment – solution conditions can be adjusted (concentration dependency, effect of pH, ionic strength, buffer type, ligands, oxidation state, temperature, etc.)
Very large size range (102 – 108 Dalton)
Dynamics - measure oligomerization states of reversible self- or hetero-associations, ligand binding, slow kinetics and Kd
Composition analysis – number of components, their partial concentration, molecular weight, and anisotropy
Conformational analysis - folding/melting studies of biopolymers, conformational changes based on changes in solution properties

---
Background – Analytical Ultracentrifugation
Available Optical Systems:
Multiple detectors extend the range of AUC applications:
UV/vis absorbance (single wavelength): all-purpose detector for biopolymers and materials absorbing in the visible. Slower detection, good for low protein concentration – measure intensity of transmitted light.
Fluorescence: Study molecules with intrinsic fluorophores or eGFP fusions in impure cell extracts, exquisite selectivity for binding experiments, add fluorescently labeled antibodies to an impure cell extract, study the order of assembly in a multi-domain protein complex – measure intensity of fluorescence emission with a confocal microscope setup (488 nm excitation)
Interference: fast data acquisition and measurement of non-absorbing molecules, carbohydrates, high-concentration studies – measure refractive index differences at 675 nm
Multi-wavelength UV/vis: obtain additional spectral dimension in addition to hydrodynamic separation for independent characterization of molecular properties – measures intensity of transmission of multiple wavelengths

---
Radial Dilution
Radial Dilution occurs because of the cell's sector shape. Molecules sedimenting towards the outside of the cell will dilute as they sediment.
All molecules - no matter at what position they are - will dilute at the same rate, causing a reduction in the observed optical density. At any given time, this dilution is the same at each point in the cell.
Radial Dilution can be observed through a reduction in the plateau absorbance in successive scans

---
Calculation of the Sedimentation Coefficient:
hat s `_b ~=~ ln {left ( {r_b`(t)} over {r_m ` (t_0)} right )} ~ left (%omega^2`(t`-t_0) right )^{`-1}
{M`left (1`-` bar v %rho` right )} over {N`f} ~ = ~ v over {%omega^2 r} ~= ~ s v ~= ~ dr over dt
dr over r ~= %omega^2 ` s ` dt int from r=m to r=b {1 over r} dr ~=~ int from t=0 to t=scan s %omega^2 dt

---
Calculation of the Sedimentation Coefficient
int from r=m to r=b {1 over r} dr ~=~ int from t=0 to t=scan s %omega^2 dt
{M`left (1`-` bar v %rho` right )} over {N`f} ~ = ~ v over {%omega^2 r} ~= ~ s
hat s `_b ~=~ ln {left ( {r_b`(t)} over {r_m ` (t_0)} right )} ~ left (%omega^2`(t`-t_0) right )^{`-1}
v ~= ~ dr over dt
dr over r ~= %omega^2 ` s ` dt

---
Calculation of the Sedimentation Coefficient
The s-value from non-midpoint boundary positions from different scans are different, because diffusion contributes to the transport in those boundary regions.

---
Calculation of the Sedimentation Coefficient
The flow due to diffusion is proportional to the concentration gradient and the diffusion coefficient (Fick's first law):
J~=~-D {partial C} over {partial x}

---
What about Diffusion and Heterogeneity?

---
van Holde – Weischet Method
Description of the Problem:
How do we distinguish between transport due to diffusion and transport due to sedimentation?
How do we distinguish boundary spreading due to heterogeneity from boundary spreading due to diffusion?
For unknown samples, can we analyze the sample in a model-independent way?

---
van Holde – Weischet Method
Key Observation by van Holde et al.:
Sedimentation is a transport process proportional to the first power of time, while Diffusion is a transport process which is proportional to the square-root power of time.
At infinity transport due to diffusion will be negligible compared to transport due to sedimentation - i.e., all components will separate out if the rotorspeed is fast enough.
van Holde, K. E. and W. O. Weischet. (1978). Boundary Analysis of Sedimentation Velocity Experiments with Monodisperse and Paucidisperse Solutes. Biopolymers, 17:1387-1403
Demeler, B. and K. E. van Holde. Sedimentation velocity analysis of highly heterogeneous systems. (2004). Anal. Biochem. Vol 335(2):279-288

---
van Holde – Weischet Analysis
Extrapolation of the same values to infinite
time by plotting vs. the inverse square-root of time
hat s `_b ~=~ ln {( {r_b`(t)} over {r_a ` (t_0)})} ~ [%omega^2`(t`-t_0)]^{`-1}
v over {%omega^2 r} ~= ~ s
dr over r ~= %omega^2 ` s ` dt

---
Radial Dilution
Radial Dilution occurs because of the cell's sector shape. Molecules sedimenting towards the outside of the cell will dilute as they sediment.
All molecules - no matter at what position they are - will dilute at the same rate, causing a reduction in the observed optical density. At any given time, this dilution is the same at each point in the cell.
Radial Dilution can be observed through a reduction in the plateau absorbance in successive scans

---
van Holde – Weischet Analysis
hat s `_b ~=~ ln {( {r_b`(t)} over {r_a ` (t_0)})} ~ [%omega^2`(t`-t_0)]^{`-1}
v over {%omega^2 r} ~= ~ s
dr over r ~= %omega^2 ` s ` dt

---
van Holde – Weischet Analysis

---
van Holde – Weischet Extrapolation Plot:

---
van Holde – Weischet Extrapolation Plot:
Scan 1 – start
of Experiment

---
van Holde – Weischet Method
Scan 10 – middle
of Experiment

---
van Holde – Weischet Method
Scan 20 – end
of Experiment

---
van Holde – Weischet Method
Division 1
(Baseline)
Boundary
Fraction = 5%

---
van Holde – Weischet Method
Division 10
(Midpoint)
Boundary
Fraction = 50%

---
van Holde – Weischet Method
Division 20
(Plateau)
Boundary
Fraction = 95%

---
van Holde – Weischet Method

---
van Holde – Weischet Method
van Holde – Weischet method:
s1:	5.35 x 10-13 (52 %)
s2:	1.87 x 10-13 (39 %)

---
Effect of Experiment Duration on Resolution

---
Effect of Rotorspeed with constant ω2t on Resolution:

---
Resolution Comparison:

---
Resolution Comparison:
van Holde – Weischet Analysis Application Examples:
Concentration dependent nonideality of s.
Aggregation and irreversible self-association
Composition Analysis
Reversibly Self-Associating Systems vs. non-interacting systems
Stoichiometry of Association
Relative quantification of individual components
Conformational information

---
Sedimentation Velocity:
Sedimentation velocity profile of a mixture of macromolecules over time

---
Sedimentation Velocity:
Composition Analysis
We can answer these questions:
How many components?

---
Sedimentation Velocity:
Composition Analysis
We can answer these questions:
How many components?
What are their molecular weights?

---
Sedimentation Velocity:
Composition Analysis
We can answer these questions:
How many components?
What are their molecular weights?
What are their shapes?

---
Sedimentation Velocity:
Composition Analysis
We can answer these questions:
How many components?
What are their molecular weights?
What are their shapes?
What is the partial concentration of each component?

---
Sedimentation Velocity:
Composition Analysis
We can answer these questions:
How many components?
What are their molecular weights?
What are their shapes?
What is the partial concentration of each component?
Do the components interact (how fast, strong)?

---
Sedimentation Velocity:
Composition Analysis
We can answer these questions:
How many components?
What are their molecular weights?
What are their shapes?
What is the partial concentration of each component?
Do the components interact (how fast, strong)?
What is the reliability of our measurement?

---
Find: partial concentration, s, D, MW, Kd, koff and f/f0
Size (relative)‏
Shape (relative)‏
[Speaker Notes: We can represent the sedimentation problem as a 2-dimensional parameter space (s and f/f0, or s and MW, or MW and f/f0, or s and D, or D and MW, or D and f/f0, etc.). Each one of these representations is valid and provides the entire information necessary to describe completely the solution properties of individual solutes. The problem is then to identify the solutes (blue dots in the plane), and their relative concentration that when combined make up the experimental data shown as a blue concentration traces for differen time and radius values.]

---
Sedimentation Velocity:
Optimization Methods:
2-dimensional Spectrum Analysis (2DSA):
Provides degenerate, linear fit to experimental data over a finite domain, identifying regions with signal in the mass/shape domain, used to remove systematic noise contributions
Genetic Algorithms (GA):
Provides parsimonious regularization of 2DSA spectrum. Satisfies Occam's razor. Also used for fitting of discrete, non-linear models (reversible association, non-ideality, co-sedimenting solutes)
Monte Carlo Analysis (MC)
Used to measure the effect of noise on the fitted parameters, yields parameter distribution statistics
Parametrically Constrained Spectrum Analysis (PCSA)
Used to regularize 2-dimensional spectrum analysis. Enforce a unique mapping of one molar mass/sedimentation coefficient per frictional ratio.