Spectroscopy

---
Absorption
1) percent transmission ( %Tl = 100 x Il/I0,l )
Reported by:
2) absorbance ( Al = log {I0,l/Il} = el c l )
Measured by:
single or double beam spectrophotometer
R
S
light source
monochromator
cuvette holder
detector

---
Significance of deviations from the Beer-Lambert Law:
If nothing happens in a solution as a function of concentration of the component solutes, that is there are no concentration-dependent interactions, then the OD should increase linearly with increases in concentration of the components (this requires that all solute components have proportional increases in concentration or that different components have equivalent extinction coefficients.
Deviations mean interactions. The change in absorbance versus concentration will follow the thermodynamics of the system, reflecting cooperativity, positive or negative, or lack thereof.

---
Aromatic Amino Acids
Trp (W) Tyr (Y) Phe (F)

---
Absorption Spectra of the Nucleic Acids

---
Hasselbacher et, al., Biophys J 60, 20 (1995)
Lakowicz, Principles Fluorescence Spectroscopy 3rd Ed., 2006

---
Tryptophan Analogs
5-fluorotryptophan 4-fluorotryptophan
5-hydroxytryptophan 7-azatryptophan
Ross et al.,Topics in Fluorescence Spectroscopy 6, Lakowicz ed. 2000

---
Tryptophan Analogs
Ross et al., Meth Enzymol 278, 151 (1998)
Ross et al., Meth Enzymol 278, 151 (1998)
Ross et al., Proc Natl Acad Sci USA 89, 12923 (1992)

---
Tryptophan Analogs
Ross et al., Topics in Fluorescence Spectroscopy 6, 17 (2000)

---
Why is this plot not linear for the entire range?
At some point the absorbance is so high that not sufficient light passes through to the detector, and linearity is no longer satisfied.
The absorbance at which an instrument becomes non-linear depends on the following factors:
Concentration of the analyte
Lamp intensity at the measured wavelength
Extinction coefficient of the analyte at measured wavelength
Sensitivity of detector at the measured wavelength
Relationship between
Absorbance and Concentration
For best accuracy, always measure between 0.1 – 1.0 OD

---
Concentration
Beer-Lambert Law (Beer’s Law): Al = el c l
most accurate range to obtain c: between 15 and 65 %T
  which is A between 0.2 and 0.8
Identification of Chromophore(s) by Spectra
Are spectra from multiple chromophores in a macromolecule additive?
A(l,sample) = aA(l,a) + bA(l,b) + gA(l,c) + dA(l,d) + …..
LINCS: LINear Combination of Spectra
approximately linear in proteins
but not linear in DNA or RNA
Investigate Interacting Systems by Difference Spectra
Quantification of Binding
Evaluation of Conformational Changes
Laws and Shore, J. Biol Chem 254, 2582 (1979)

---
PRINCIPLES OF FLUORESCENCE SPECTROSCOPY
Born in County Sligo, Ireland, Stokes was the Lucasian Professor of Mathematics at Cambridge from 1849 until his death in 1903.
Some major contributions:
Fluid dynamics (Stokes’ Law)
Wave theory of light
Polarization of light
Fluorescence of minerals
Stokes’ line (Raman scatter)
Sir George Stokes
1819-1903
Lakowicz, Principles Fluorescence Spectroscopy 3rd Ed., 2006

---
Jabłonski Diagram
Time Scales
Si
Abs.: ~ 10 –15 s
IC.: < 10 –12 s
Fluor: ~ 10 –9 s
S3
Frank-Condon state
S2
S1
S0
Absorption
E = h
   Internal
Conversion
Fluorescence

---
Lakowicz, Principles Fluorescence Spectroscopy 3rd Ed., 2006

---
Jabłonski Diagram
Time Scales
Si
Abs.: ~ 10 –15 s
IC.: < 10 –12 s
Fluor: ~ 10 –9 s
ISC: ~ 10 –9 s
S3
Frank-Condon state
S2
S1
S0
Absorption
E = h
   Internal
Conversion
S0
T1
T2
Intersystem
   Crossing
Fluorescence

---
Jabłonski Diagram
Si
Abs.: ~ 10 –15 s
IC.: < 10 –12 s
Fluor: ~ 10 –9 s
ISC: ~ 10 –9 s
Phos: > 10 –6 s
S3
Frank-Condon state
S2
S1
S0
Absorption
E = h
   Internal
Conversion
S0
T1
T2
Intersystem
   Crossing
Fluorescence
Phosphorescence

---
Single Trp Residue in Cod Parvalbumin; 77 K
Absorbance
Fluorescence
Phosphorescence
250 300 350 400 450 500
wavelength (nm)
Relative Intensity or Absorbance

---
Loss of Energy from Excited State back to Ground State
- Internal Conversion (IC; mainly through vibrational relaxation)
- Quenching: collisions with solvent, solutes, or groups of chromophore
- Intersystem Crossing (ISC)
phosphorescence from long-lived triplet state
- Förster Resonance Energy Transfer (FRET)
- Emission of a photon
fluorescence from lower energy than from initial Frank-Condon state;	Stoke’s shift
Excited-State Reactions

---
Excited-State Reactions
- Bond Breaking (UV, x-ray)
- Bleaching
reactions with O2, etc.
photorecovery experiments
- Labeling Reactions
- Generation of New Emitters
proton transfer (A* ↔ B-* + H+)
        excimer formation (excited-state dimer: A*+ A ↔ A A*)
Solvent (dipolar) Relaxation
        S1 → S1´ → → S1´´ → → → S1´´´ → → → → …..

---
Lifetime and quantum yield
τ = 1 / (Kf + Σ Knr)	excited-state lifetime
ϕ = Kf / (Kf + Σ Knr)	excited-state quantum yield
Fλ = ϕ Aλ = ϕ el c l	fluorescence intensity
Σ Knr = IC + ISC + e- transfer + ….. other dynamic processes

---
Lakowicz, Principles Fluorescence Spectroscopy 3rd Ed., 2006

---
Lakowicz, Principles Fluorescence Spectroscopy 3rd Ed., 2006

---
Raman scatter &
   Trp emission
WAVELENGTH (nm)
Lakowicz, Principles Fluorescence Spectroscopy 3rd Ed., 2006
EMISSION INTENSITY

---
Primary and secondary inner filter errors:
Fcorr = Fobs log ((ODex + ODem) /2)
Lakowicz, Principles Fluorescence Spectroscopy 3rd Ed., 2006

---
        Geometry considerations:
most common is center focus (upper left and upper middle)
front-face illumination, used for optically thick samples, should be either at 30° or 60°, not 45°. Excitation reflection angle makes this obvious.
Lakowicz, Principles Fluorescence Spectroscopy 3rd Ed., 2006

---
Valeur and Berbaran-Santos, Molecular Fluorescence,
2nd Ed., 2012
Lakowicz, Principles Fluorescence Spectroscopy 3rd Ed., 2006

---
Excited-State Reactions: Dipolar Relaxation
Lakowicz, Principles Fluorescence Spectroscopy 3rd Ed., 2006

---
Excited-State Reactions: Dipolar Relaxation
Lakowicz, Principles Fluorescence Spectroscopy 3rd Ed., 2006

---
Absorption and Emission Transition Dipole Moments
X
Y
Z
S0 S1
S0 S2

---
Absorption and Emission Transition Dipole Moments
X
Y
Z
S0 S1
S1 S0
S0 S2

---
Absorption and Emission Transition Dipole Moments
Anisotropy (Jabłonski, 1960):
r = (IV – IH)/(IV – 2 IH) = (IV - IH)/Itotal)
depends on the angle, , between absorption and emission transition moments
X
Y
Z
S0 S1
S1 S0
S0 S2


---
Absorption and Emission Transition Dipole Moments
Principle of Photoselection (Albrecht, 1961)
Andreas Albrecht, 1927-2002
Anisotropy (Jabłonski, 1960):
r = (IV - IH)/Itotal )
depends on the angle, , between absorption and emission transition moments
with random molecular orientation r0 = (3cos2q -1)/5
    if  = 0 (parallel), then r0 = 0.4
or if  = 90 (perpendicular), then r0 = -0.2
X
Y
Z
S0 S1
S1 S0
S0 S2


---
Principle Polarization Spectrum
Determination of r0 as a function of excitation wavelength
at a constant em
prevent depolarizing motions
scan ex for all 4 sets of polarizer angles
calculate and plot r0 vs ex
permanent dipole
moment in S0 of
~ 2 debye
see Figs. 10.6, 10.7, 10.29 in Lakowicz (2nd ed.)
Information obtained
r0 for different electronic transitions
thus calculate  between abs. and em. dipole moments
as in indole, find ‘hidden’ transitions 
for indole spectrum, see Fig. 10.8 in Lakowicz (2nd ed.)
N
1La
1Lb

---
Principle Polarization Spectrum
Lakowicz, Principles Fluorescence Spectroscopy 3rd Ed., 2006

---
Anisotropy and Photoselection
Lakowicz, Principles Fluorescence Spectroscopy 3rd Ed., 2006

---
Anisotropy and Photoselection
Lakowicz, Principles Fluorescence Spectroscopy 3rd Ed., 2006

---
Anisotropy and Photoselection

---
Anisotropy and Photoselection
Magic Angle conditions
Itotal = Ix + Iy + Iz = Ix + 2 Iy
Iviewed = Ix cos2 θ + Iy cos2 (90° - θ)
Iviewed will be proportional to Itotal if
[cos2 (90° - θ)]/(cos2 θ) = tan2 θ = 2
then	θ = 54.7°
Badea and Brand, Meth Enzymol 61, 378 (1979)

---
Anisotropy and Fluorescence
Interactions (binding) and addition laws
Ftotal = FV + 2 FH
Ftotal = ∑fi = ∑ϕi ai = ∑ϕi ei ci l
FRtotal = ∑fi ri = ∑ϕi ai ri leads to the non-addition law:
Rtotal ≠ ∑ri (except under special circumstances)

---
Jean B. Perrin
Francis Perrin
J. Robert Oppenheimer
Theodor Förster
1870-1942
1901-1992
1904-1967
1910-1974
Lakowicz, Principles Fluorescence Spectroscopy 3rd Ed., 2006
Held, BioTek.com, 2005

---
Resonance Energy Transfer
Lakowicz, Principles Fluorescence Spectroscopy 3rd Ed., 2006

---
Resonance Energy Transfer
The orientation factor, k2
The orientation factor, k2 can be calculated from the projections of the 9 combinations of donor and acceptor axes (draw projection of donor axes on acceptor axes):
1 orientation where k2 = 4
2 orientations where k2 = 1
6 orientations where k2 = 0
3 of the 9 combinations contribute to FRET: åk2 = (1 x 4) + (2 x 1) = 6
6 of 9 total combinations do not contribute to FRET: åk2 = 0
So the average k2 for all combinations is 6/9 = 2/3

---
Water Packs Better Against a Protein Surface
Than Another Protein (or DNA) Does

---
IHF : sequence-specific interaction
Senear, et al, (2007) Nucleic Acid Res 35: 1761
Rice, P.A., et al, (1996) Cell 87: 1295-1306